## Slide 1: How do packet delay and loss occur?
packets queue in router buffers, waiting for turn for transmission
  queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 2: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 3: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different

## Slide 4: Caravan analogy
car ~ bit; caravan ~ packet; toll service ~ link transmission
toll booth takes 12 sec to service car (bit transmission time)
“propagate” at 100 km/hr
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
ten-car caravan
(aka 10-bit packet)
100 km
100 km
toll booth
toll booth

## Slide 5: Caravan analogy
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth

## Slide 6: Packet queueing delay (revisited)
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”

## Slide 7: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 8: Packet loss
queue (buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation (on publisher’s website) of queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 9: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 10: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 11: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/