## Slide 1
Analog/Digital Conversions
Analog data are a function of time and occupy a limited frequency spectrum; such data can be represented by an electromagnetic signal occupying the same spectrum.
Digital data can be represented by digital signals, with a different voltage level for each of the two binary digits
But these are not the only possibilities
Digital data can also be represented by analog signals by use of a modem (modulator/demodulator)
Similarly, analog data can be represented by digital signals. The device that performs this function for voice data is a codec (coder-decoder)

## Slide 2
Analog/Digital Conversions
Data stored in the computer is in the form of 0’s and 1’s. To be carried from one place to the other, data is usually converted to digital signals.
  This is called “Digital-to-Digital Conversion” or “Encoding digital data into digital signals”
Sometimes we need to convert analog data to the digital signal, for example, conversion of telephone conversation to digital signal for different reasons, like to decrease effect of noise
  This is called “Analog-to-Digital Conversion” or “Digitizing an Analog Signal”

## Slide 3
Analog/Digital Conversions
We might want to send a digital signal coming out of computer through a medium designed for analog signals, for example, to send data from one place to the other using a telephone line.
  This is called “Digital-to-Analog Conversion” or “Modulating a digital Signal”

## Slide 4
Analog/Digital Conversions
Often an analog signal is sent over long distances using analog media, for example, voice or music from a radio station which is an analog signal is transmitted through the air, however the frequency of voice or music is not, suitable for this kind of transmission.
The signal should be carried by a higher frequency signal. This is called “Analog-to-Analog Conversion” or “Modulating an analog Signal”

## Slide 5
Analog/Digital Conversions

## Slide 6: Types of Conversions Digital to digital Analog to digital Digital to analog Analog to analog

## Slide 7: Digital-To-Digital Conversion
Representation of digital data by using digital signals
Techniques for digital-to-digital conversion
  Line coding
  Block coding
  Scrambling

## Slide 8: Digital-To-Digital Conversion
Line Coding: the process of converting digital data to digital signals
Assumption: Data is stored in computer memory as sequence of bits
Line coding converts sequence of bits to digital signals
For example when we transmit data from computer to the printer, both original and transmitted data have to be digital
Encoding a digital signal is where 1’s and 0’s generated by the computer are translated into voltage pulses that can be propagated over the wire

## Slide 9: Digital-To-Digital Conversion
Line Coding
At sender: encoding of digital data into digital signal
At receiver: recreation of digital data by decoding the digital signal

## Slide 10: Digital-To-Digital Conversion
Characteristics of Line Coding Schemes
Signal element versus data element
A data element is the smallest entity (bit) that can represent a piece of information
  In data communications, our goal is to send data elements which are what we need to send
  Data elements are being carried
A signal element is the shortest unit (time wise) of a digital signal
  In digital data communications, a signal element carries data elements (carriers)
  So signals elements are what we can send
  Ratio of data elements to signals elements

## Slide 11: Digital-To-Digital Conversion
Characteristics of Line Coding Schemes
Signal element versus data element
In the simplest case, there is a one-to-one correspondence between bits and signal elements

## Slide 12: Digital-To-Digital Conversion
Characteristics of Line Coding Schemes
Data rate versus signal rate
The data rate (bit rate) is the number of data elements (bits) sent in I second
  The unit is bits per second (bps)
The signal rate (baud rate, modulation rate or pulse rate) is the number of signal elements sent in I second.
  The unit is the baud
Data communications goal: increase the data rate (increasing speed of transmission) and decrease the signal rate (decreasing bandwidth requirement)

## Slide 13: Digital-To-Digital Conversion
Characteristics of Line Coding Schemes
Bandwidth
Although the actual bandwidth of a digital signal is infinite, the effective bandwidth is finite
the baud rate, not the bit rate, determines the required bandwidth for a digital signal
The bandwidth reflects the range of frequencies we need

## Slide 14: Digital-To-Digital Conversion
Characteristics of Line Coding Schemes
Baseline wandering
A long string of 0s or 1s can cause a drift in the baseline (baseline wandering) and make it difficult for the receiver to decode correctly
A good line coding scheme needs to prevent baseline wandering

## Slide 15: Digital-To-Digital Conversion
Characteristics of Line Coding Schemes
Self synchronization
To correctly interpret the signals received from the sender,
  the receiver's bit intervals must correspond exactly to the sender's bit intervals.
If the receiver clock is faster or slower
  the bit intervals are not matched and the receiver might misinterpret the signals
Consider a situation where the receiver has a shorter bit duration
  Let the sender sends 10110001, while the receiver receives 110111000011

## Slide 16: Digital-To-Digital Conversion
Characteristics of Line Coding Schemes
Self synchronization
A self-synchronizing digital signal includes timing information in the data being transmitted
  The same can be achieved by adding transitions in the signal that alert the receiver to the start, middle or end of the pulse.
  These points can reset the clock in case the receiver’s clock is out of synchronization

## Slide 17
Effect of lack of synchronization
Consider a situation where the receiver has a shorter bit duration
Let the sender sends 10110001, while the receiver receives 110111000011

## Slide 18
In a digital transmission, the receiver clock is 0.1 percent faster than the sender clock. How many extra bits per second does the receiver receive if the data rate is 1 kbps?
How many if the data rate is 1 Mbps?
Solution
At 1 kbps, the receiver receives 1001 bps instead of 1000 bps.
Example
At 1 Mbps, the receiver receives 1,001,000 bps instead of 1,000,000 bps.

## Slide 19: Digital-To-Digital Conversion
Characteristics of Line Coding Schemes
Built-in error detection
Desirable to have a built-in error-detecting capability in the generated code to detect some of or all the errors that occurred during transmission
Immunity to noise and interference
Desirable to have a code that is immune to noise and other interferences
Complexity
A complex scheme is more costly to implement than a simple one
Example: a scheme that uses four signal levels is more difficult to interpret than one that uses only two levels

## Slide 20: Digital-To-Digital Conversion
Line Coding Schemes (types of encoding)

## Slide 21: Line Coding Schemes: Unipolar
Unipolar: non-return-to-zero (NRZ) [no return in middle]
  Encoding is simple , with only one technique in use
  all the signal levels are on one side of the time axis, either above or below
  It is called Unipolar because it uses only one polarity
  positive voltage defines bit 1 and the zero voltage defines bit 0

## Slide 22: Practice Example
Convert the following data elements (bit stream) into digital signals using Unipolar Scheme
11001101

## Slide 23: Line Coding Schemes: Polar
Polar
  Polar encoding uses two voltage levels, positive and negative (on both sides of time axis)
    The voltage level for 0 bit can be positive (+ve) and the voltage level for 1 can be negative
  3 subcategories: NRZ, RZ, Biphase

## Slide 24: Line Coding Schemes: Polar
Polar: NRZ
Non-return-to-zero-level (NRZ-L)
  A +ve voltage means the bit is a 0 and a –ve voltage means the bit is a 1 (vice versa may also be true)

## Slide 25: Line Coding Schemes: Polar
Polar: NRZ : Non-return-to-zero-Invert (NRZ-I)
the change or lack of change in the level of the voltage determines the value of the bit
  If there is no change, the bit is 0;
  if there is a change, the bit is 1
  A transition (low-to-high or high-to-low) at the beginning of a bit time denotes a binary 1 for that bit time; no transition indicates a binary 0

## Slide 26: Practice Example
Convert the following data elements (bit stream) into digital signals using NRZ-I Scheme
10101100

## Slide 27
NRZ-L and NRZ-I both have a DC component problem and baseline wandering, it is worse for NRZ-L. Both have no self synchronization &no error detection. Both are relatively simple to implement.

## Slide 28: Line Coding Schemes: Polar
Polar: Return-to-zero (RZ)
  Any time, data contains long strings of 1’s or 0’s, receiver can loose its timing (synchronization problem of NRZ)
  One solution is RZ encoding which uses 3 values; Positive, Negative and Zero
  Signal changes not between bits but during each bit

## Slide 29
  Here, +ve voltage means 1 and a –ve voltage means 0,
  but unlike NRZ-L, half way through each bit interval, the signal returns to zero
  A 1 bit is represented by positive to zero and a 0 is represented by negative to zero transition
Line Coding Schemes

## Slide 30
Convert the following data elements (bit stream) into digital signals using Polar RZ Scheme
10101100
Practice Example

## Slide 31
  Problem with RZ
  Main problem with RZ encoding is that it requires two signal changes to encode one bit
    therefore occupies more bandwidth
    But it is most effective solution so that receiver cannot lose timing (no DC component problem)
  Complexity: uses three levels of voltage
Line Coding Schemes

## Slide 32
Biphase
  Best existing solution to the problem of synchronization
  Signal changes at the middle of bit interval but does not stop at zero
    Instead it continues to the opposite pole
There are two types of biphase encoding
    Manchester
    Differential Manchester
Line Coding Schemes: Polar

## Slide 33
  Biphase: Manchester
Transition in middle of each bit period
Transition serves as clock and data
Used by IEEE 802.3 (10Mbps Ethernet)
Negative-to-Positive Transition (low to high) = 1
Positive-to-Negative Transition (high to low) = 0
Line Coding Schemes: Polar

## Slide 34
Convert the following data elements (bit stream) into digital signals using Biphase Manchester encoding Scheme
10101100
Practice Example

## Slide 35
  Biphase: Differential Manchester
Midbit transition is clocking only (for synchronization)
• Transition at start of a bit period represents zero
• No transition at start of a bit period represents one
• Note: this is a differential encoding scheme
• Used by IEEE 802.5 (Token ring)
Line Coding Schemes: Polar

## Slide 36
Line Coding Schemes: Polar

## Slide 37
Convert the following data elements (bit stream) into digital signals using Biphase Differential Manchester encoding Scheme
10101100
Practice Example

## Slide 38
  Bipolar encoding
  There are three voltage levels; +ve, -ve, zero to represent the symbols (note not transitions to zero as in RZ)
  Voltage level for one symbol is at “0” and the other alternates between +ve & -ve.
  Bipolar Alternate Mark Inversion (AMI): the “0” symbol is represented by zero voltage and the “1” symbol alternates between +V and -V.
  Pseudoternary is the reverse of AMI: the “1” symbol is represented by zero voltage and the “0” symbol alternates between +V and -V
Line Coding Schemes: Bipolar

## Slide 39
  Bipolar encoding
  Bipolar Alternate Mark Inversion (AMI) and Pseudoternary
Line Coding Schemes: Bipolar

## Slide 40
Convert the following data elements (bit stream) into digital signals using AMI and Pseudoternary Scheme
10101100
Practice Example

## Slide 42
Alternate Mark Inversion(AMI)
  Pros and Cons:
  There will be no loss of synchronization if a long string of 1s occurs
  Each 1 introduces a transition, and the receiver can resynchronize on that transition
  A long string of 0s would still be a problem
  No error detection