## Slide 1
Data Link Layer
The data link layer is responsible for moving frames from one hop (node) to the next

## Slide 2: Functions of the Data Link Layer (local focus)
Specific things that DLL does in order to accomplish the general functions of handling errors and regulating data flow
  Framing: divides the stream of bits received from the network layer into manageable data units called frames
  Error Control: adds reliability to the physical layer by adding mechanisms to detect and retransmit damaged, duplicate, or lost frames. Both detection and correction schemes may be used
Flow Control (imposes a flow control mechanism to prevent sender from “swamping” or overwhelming the receiver which is normally built into the protocol
Media access control determines which device has control over the link at any given time when two or more devices are connected to the same link
Addressing adds a header to the frame to define the addresses of the sender and receiver of the frame

## Slide 3
Data link layer divided into two functionality-oriented sub-layers
Data link control and
Medium Access Control
The Medium Access Control Sub-layer

## Slide 4: Medium Access Control
There are Two categories of network links
Those using point-to-point connections
Those using broadcast channels
In any broadcast network
How to determine who gets to use the channel when there is competition for it?
Broadcast channels are sometimes referred to as multi-access channels or random access channels
Multiple-access problem: when a channel is shared among many nodes, the problem arises to when each node should access the channel
Protocols used to determine who goes next on a multi-access channel belongs to MAC layer
  Distributed system is the key matter which makes this issue hard as there is no one in-charge in the system

## Slide 5: MAC Protocols
MAC is important in LANs, particularly critical to the performance of wireless LANs as wireless is naturally an open, shared, and broadcast medium/channel
MAC allows several stations connected to the transmission medium to transmit over it and to share its capacity
A MAC protocol is used to resolve potential contention and collision when using the communication medium
  MAC protocols define rules to force distributed nodes to access wireless medium in an orderly and efficient manner

## Slide 6: Ingredients of MAC Protocols
Carrier sense (CS)
Hardware capable of sensing whether transmission taking place in vicinity
Acknowledgments
  When collision detection not possible, link-layer mechanism for identifying failed transmissions
Backoff mechanism
  Method for estimating contention and deferring transmissions
Collision detection (CD)
  Hardware capable of detecting collisions
Collision avoidance (CA)
  Protocol for avoiding collisions

## Slide 7: Propagation Vs Transmission
Propagation | Transmission
How long it takes one bit to travel from one end of the medium to the other or time it takes the signal to travel from source to destination | How long it takes to get all the bits into the medium in the first place or time it takes the sender to transmit all bits of the packet
It is proportional to the length of the medium (length/speed or distance/speed) | It is ----- packet length/data rate
Propagate means to move something in a medium..... | Transmit means to send something.......
Therefore, propagation delay is the time taken by an object to pass through a medium | Whereas transmission delay is the time taken to transfer something
It depends on the distance between source and receiver and also the medium through which it is travelling | It depends on the length of object which is to be transmitted and the rate at which the object is transmitted

## Slide 8: Propagation Vs Transmission
Packet transmission time: Example
  Consider a 100 Mbit/s Ethernet, and the maximum packet size of 1520 bytes
  Then Maximum packet transmission time
    1520*8 bit / (100 000 000 bit/s) =----- μs
Packet propagation time: Example
  Consider wireless communication with maximum distance of 100 meter between sender and receiver
  Then Maximum link propagation delay
  ≈ 100 m / (300 000 000 m/s) = ---- μs

## Slide 9: Example
A 1000 byte packet is sent from your home to a server. It is first sent over a 10 Mbps wireless link. Once it has been received completely, it is then sent over a 100 Mbps ISP link. The propagation delay of the wireless link is 500 nanoseconds and the propagation delay of the ISP link is 10ms. How long does it take (in milliseconds) for the packet to reach the server?

## Slide 10
Taxonomy of multiple-access protocols

## Slide 11: Random multiple access protocols
In random access or contention methods,
  No station is superior to another station and
  No station is assigned the control over another
  No station permits, or does not permit, another station to send
  At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send
  A station can transmit
    When it desires
    Provided it obeys the mechanism defined by the protocol
      Such as verification of state of medium

## Slide 12: Random multiple access protocols
Stations transmit without any schedule
Methods are called random access because
  transmission is random among the stations
Also called contention methods
  Stations have competition to access the common medium that can lead to conflicts
  no rules specify which station should transmit next
Access collision
  If more than one stations try to send
    Frames can be either destroyed or modified

## Slide 13: Random multiple access protocols
To avoid access collision or resolve when it happens, a node follows a procedure that tackles the following:
  When to access the medium
  What to do if medium busy
  How to determine the transmission failure or success
  What to do in the situation of collision

## Slide 14: ALOHA Network (Areal LOcations of Hazardous Atmospheres)
Principal of pure ALOHA:
If you have data to send, send the data
If the message collides with another transmission (no ACK received), sender waits random time before trying again (resend)
Norm Abramson devised a new protocol at the University of Hawaii for multiple access
  When should nodes send?
computer network connecting the Hawaiian islands in the late 1960s with wireless links
Use of very simple procedure: Multiple access
All random access methods evolved from ALOHA

## Slide 15
Frames in a pure ALOHA network:
4 stations each with 2 frames contending with one another for access to the shared channel

## Slide 16: Pure ALOHA
Even if one bit of a frame coexists on the channel with one bit from another frame: There is a collision
Resend the frames that have been destroyed during transmission
It relies on ACKs from receiver
  If no ACK received after a time-out period, then assumes that frame has been destroyed and resend the frame
If all collided stations retransmit after time out: Frame may collide again
Pure ALOHA dictates that each station waits a random amount of time (back-off time:TB) before resending its frame
  The randomness helps in avoiding more collisions
To prevent congestion of the channel with retransmitted frames
  a station must give up after a maximum number of retransmission attempts Kmax and try later

## Slide 17
Procedure for pure ALOHA protocol

## Slide 18: Pure ALOHA: Example
The stations on a wireless ALOHA network are a maximum of 600 km apart. If we assume that signals propagate at 3 × 108 m/s, we find
⮚ Tp = (600 × 103 ) / (3 × 108 ) = 2 ms
⮚ Value of TB for different values of
K = 1, 2, 3
⮚ For K = 2,
⮚ the range is {0, 1, 2, 3}
⮚ This means that TB can be 0, 2, 4, or 6 ms, based on the outcome of the random variable
⮚ For K = 3,
⮚ the range is {0, 1, 2, 3, 4, 5, 6, 7}
⮚ This means that TB can be 0, 2, 4, . . . , 14 ms based on the outcome of the random variable

## Slide 19: Pure ALOHA
Under what conditions will frame A arrive undamaged?
Let Tfr be the time required to send one frame
If any other user has generated a frame between t-Tfr and t, the end of that frame (here B) will collide with beginning of A
Similarly, any other frame started between t and t+Tfr will bump into the end of frame A for station B’s frame to be transmitted without any problems, nobody has to be transmitting from time t-Tfr and time t+Tfr, which is 2 times the frame transmission time So Pure ALOHA vulnerable time = 2 x Tfr

## Slide 20: Example
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the requirement to make this frame collision-free?
Answer
Average frame transmission time
Tfr = 200 bits/200 kbps = 1 ms (data/capacity)
The vulnerable time is 2 × 1 ms = 2 ms
This means no station should send later than 1 ms when this station
starts transmission and It means previous transmission must end before its start no station should start sending during the 1 ms period that this station is sending

## Slide 21: Pure ALOHA Example
On a wireless ALOHA network
  stations are maximum 300 Km apart
  Assume that signals propagate at 3 x 108 m/s
  Maximum propagation time= Tp = ?
  Backoff time = TB = ? If K = 1, 2,3
What will be the maximum propagation time and backoff time if stations are 900 Km apart

## Slide 22: Slotted ALOHA
Slotted ALOHA was invented to improve the efficiency of pure ALOHA
In slotted ALOHA, time is divided into slots of Tfr seconds (average transmission time for a frame) and force the station to send only at the beginning of the time slot
  A station must wait until the beginning of the next time slot
    If it misses to transmit at the start of a time slot
Possibility of collision
  If two stations try to send at the start of the same time slot

## Slide 23
Frames in a slotted ALOHA network

## Slide 24: CSMA (Carrier Sense Multiple Access)
CSMA protocol was developed to minimize the chances of collision, so as to improve the performance
Improves ALOHA by listening for activity before we send (carrier sense)
Protocols in which station listen for a carrier (such as an electrical bus, or a band of the electromagnetic spectrum) and act accordingly are called carrier sense protocols
Collision chances can be reduced to great extent
  if a station senses the channel before trying to use it
So CSMA is based on the principal of sense before transmit
  If channel sensed idle, transmit entire frame
  If channel sensed busy, defer transmission
  Human analogy: don’t interrupt others

## Slide 25: CSMA
CSMA cannot eliminate the possibility of collision completely
  it can only reduce the chances of collision
Collision is possible if two nodes send instantaneously (simply)
BUT a collision is still possible even if they send at slightly different times
  it takes time for frames to propagate along the medium
The propagation delay is the major concern for the chances of collision

## Slide 26: CSMA
Let station B senses the medium at t1 and finds it idle,
  so it sends a frame
At time t2 (t2> tI)‘station C senses the medium and finds it idle
  because, at this time, the first bits from station B have not reached station C
  So, C also sends a frame
The two signals collide and both frames are destroyed
CSMA Access Modes
  1-persistent CSMA
  Non-persistent CSMA
  P-persistent CSMA

## Slide 27: 1-Persistent CSMA
station that wants to transmit data, continuously senses the channel to check whether it is idle or busy
If the channel is busy
  the station continues sensing until it becomes idle
When an idle channel is detected
  The station immediately transmits the frame with probability 1 (so called1-persistent CSMA)
It has the highest chance of collision
  two or more stations may find channel to be idle at the same time and transmit their frames
  When the collision occurs, the stations wait a random amount of time and start all over again
  This mode is used in CSMA/CD

## Slide 28
Drawback 1-Persistent CSMA
The propagation delay time greatly affects this protocol
  Let us suppose, just after the station 1 begins its transmission, station 2 also becomes ready to send its data and sense the channel
  If the signal of station 1 has not yet reached station 2, station 2 will sense the channel to be idle and will begin its transmission. This will result in collision
Even if propagation delay time is zero, collision will still occur
  If two stations become ready in the middle of third station’s transmission
  both stations will wait until the transmission of first station ends and both will begin their transmission exactly simultaneously resulting in collision

## Slide 29
A station that has a frame to send senses the channel
  If the channel is idle,
    it sends immediately
  If the channel is busy,
    it waits a random amount of time, and
    then senses the channel again
  In non-persistent CSMA the station does not continuously sense the channel for the purpose of capturing it when it detects the end of precious transmission
Non-Persistent CSMA

## Slide 30
Advantages of non-persistent
It reduces the chances of collision
  because the stations wait a random amount of time
It is unlikely that two or more stations will wait for same amount of time and will retransmit at the same time
Disadvantages of non-persistent
It reduces the efficiency of network
  because the channel remains idle when there may be station with frames to send
This is due to the fact that the stations wait a random amount of time after the collision
Non-Persistent CSMA

## Slide 31
This method is used when channel has time slots such that the time slot duration is equal to or greater than the maximum propagation delay time
Whenever a station becomes ready to send, it senses the channel
  If channel is busy, station waits until next slot
  If the channel is idle, it transmits with a probability p
  With the probability q=1-p, the station then waits for the beginning of the next time slot
  If the next slot is also idle, it either transmits or wait again with probabilities p and q respectively
  This process is repeated till either frame has been transmitted or another station has begun transmitting
  In case of the transmission by another station, the station act as though a collision has occurred and it waits a random amount of time and starts again
  This mode is used in CSMA/CA
Advantage: it reduce collision chances and improve the efficiency of the network
P-Persistent CSMA

## Slide 32
Flow diagram for three persistence methods

## Slide 33
Behavior of three persistence methods

## Slide 34
CSMA does not specify any procedure after collision
CSMA/CD enhances the algorithm to handle the collision

## Slide 35: CSMA/CD (carrier sense multiple access/ collision detection)
Persistent and non-persistent CSMA protocols are definitely an improvement over ALOHA because they ensure that no station begins to transmit while the channel is busy
However, if two stations sense the channel to be idle and begin transmitting simultaneously, their signals will still collide.
Another improvement (on top of ALOHA) is for the stations to quickly detect the collision and abruptly stop transmitting, (rather than finishing them).This scheme saves time and bandwidth

## Slide 36: CSMA/CD
When a sender detects a collision, it sends a “jam signal”.
  Make sure that all nodes are aware of the collision
  Length of the jam signal is 32 bit times
In CSMA/CD, stations abort their transmission when they detect a collision e.g., Ethernet, IEEE802.3
It is not applicable to wireless systems

## Slide 37: CSMA/CD: Procedure
Node has a frame to transmit
Sense the medium
  If busy (not idle): wait until becomes free
  If idle: transmit
After transmission, check weather collision has occurred
  If collision has detected
    Send a jam signal
    Increment retransmission counter
    Check maximum number of retransmission attempts. If yes, abort transmission
    Based on number of collisions, calculate random backoff time and wait that time
    Repeat from step 2 again
  If no collision detected, transmission is successful
Retransmission counters are reset and end frame transmission

## Slide 38
Flow diagram for the CSMA/CD

## Slide 39
Energy level during transmission, idleness, or collision
level of energy in a channel can have three values
  Zero: the channel is idle
  Normal: The station has successfully captured the channel and is sending its frame
  Abnormal: there is a collision and the level of the energy is twice the normal level
station that has a frame to send or is sending a frame needs to monitor the energy level to determine if the channel is idle, busy, or in collision mode

## Slide 40
Collision detection: If the signal, the sender reads back, is different from the signal it is putting out, it knows that a collision is occurring
In fact, a received signal must not be tiny compared to the transmitted signal
In CSMA/CD : a station needs to be able to receive while transmitting to detect a collision
When there is no collision, the station receives one signal: its own signal
When there is a collision, the station receives two signals: its own signal and the signal transmitted by a second station
To distinguish between these two cases, the received signals in these two cases must be significantly different

## Slide 41
In a wired network, the received signal has almost the same energy as the sent signal because
So in a collision, the detected energy almost doubles
Popular CSMA scheme and its variant CSMA/CD developed for wired networks
  Can not be used directly in wireless networks

## Slide 42
CSMA/Collision Avoidance
Timing in CSMA/CA

## Slide 43
CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send. A station cannot send unless it has been authorized by other stations. Three popular controlled-access methods are Reservation, Polling and Token Passing
CHANNELIZATION
Channelization is a multiple-access method in which the available bandwidth of a link is shared in time, frequency, or through code, between different stations. channelization protocols are Frequency-Division Multiple Access (FDMA), Time-Division Multiple Access (TDMA) and Code-Division Multiple Access (CDMA)